## Slide 1: Integrating Building Plans into a Campus Map
David Zubenko

## Slide 2: Overview
This project looked at how building plans can be integrated into a campus map
Unfortunately many problems arose that prevented the project from being completed
This presentation will document what I was able to accomplish and how it can be used as a basis for future efforts

## Slide 3: OPP Data
OPP provided .dwg (AutoCAD) files for Willard and Findlay buildings
This data can be brought into ArcMap

## Slide 5: OPP Data - Formatting
Once the data has been brought into ArcMap the first step should be to convert the desired information into shapefile format
The polyline layer contains the information for the actual plans themselves

## Slide 7: OPP Data - Formatting
This data can be exported to a shapefile using the Data -> Export Data feature

## Slide 9: OPP Data - Formatting
The labels can also be exported to a shapefile by using the Feature Class to Shapefile tool

## Slide 10: OPP Data - Formatting
This will create a point shapefile with the accurate location of the labels

## Slide 11: OPP Data - Formatting
The desired information can be extracted from the attribute table of the shapefile
This is as far as I was able to get in regard to labels

## Slide 12: OPP Data - Simplification
The next step is to simplify the data, so it is more visually pleasing and contains less information for the GeoJSON that it will ultimately be converted into
Ultimately I was not able to come up with a good way to do this, so your guess is as good as mine
However, it is important to note that this should be done before a coordinate system is defined

## Slide 13: OPP Data – Coordinate Systems
When the data is originally brought into ArcMap it does not have a coordinate system. Therefore, a coordinate system must be defined
The “Define Projection” tool under the Data Management toolbox is the best way to do this
  NAD 1983 State Plane Pennsylvania North FIPS 3701 (Feet) is the correct coordinate system

## Slide 14: OPP Data – Coordinate Systems
However, this is not the final coordinate system
Interactive online maps are in the WGS 1984 coordinate system, so all data must be re-projected to this coordinate system
This is best done by defining the coordinate system for the layer as WGS 1984, and then exporting the data using the same coordinate system as the data frame

## Slide 15: OPP Data – Coordinate Systems
The units for NAD 1983 State Plane Pennsylvania North FIPS 3701 (Feet) are feet (obviously), while the units for WGS 1984 are decimal degrees
This can be used as a check to make sure the data is in the correct coordinate system

## Slide 16: OPP Data – GeoJSON
The next step is to convert the shapefile into a GeoJSON (Java Script Object Notation)
Although this can theoretically be done through ArcGIS or QGIS, I had the most success using the website http://ogre.adc4gis.com

## Slide 18: OPP Data – GeoJSON
The result of the tool is a text file that contains the GeoJSON information
The website http://geojson.io can be used to see if the information is accurate

## Slide 21: OPP Data – GitHub
The next step is to upload the GeoJSON to GitHub
This is done by defining a repository and then a branch and then a folder
For more information ask Aaron

## Slide 23: OPP Data – GitHub
Each file has a “raw” feature, including a url

## Slide 24: OPP Data – GitHub
This url is then put into the converter at www.rawgit.com

## Slide 26: OPP Data – JSFiddle
The new url can be added to the campus map on JSFiddle

## Slide 28: OPP Data
This is as far as I was able to get

## Slide 29: Google Indoor Maps
Another possible solution is Google Indoor Maps
This is a service Google has that allows individuals to upload floor plans that are then added to Google Maps
This service can be used for public spaces only

## Slide 37: The End